## Slide 1
PROJECT PROPOSAL • MEASUREMENT-DRIVEN
PS vs PS
UDP server performance on the
PYNQ-Z2
Python per-packet baseline vs Linux C batched I/O
Same ARM processor • same PS GEM • same Ethernet jack
A fair, reproducible comparison—not a claimed result
PYTHON
recvfrom + sendto
VS
C BATCHED
recvmmsg + sendmmsg
One board. One network path.
Change only the server strategy.
PYNQ-Z2 | Zynq-7000 PS | Linux UDP

## Slide 2
01 | FRAMING
Project in one slide
A practical PS-vs-PS experiment using the PYNQ-Z2 hardware you already have.
PYNQ-Z2 | PS UDP performance study
02
THE BOARD
The built-in RTL8211E Ethernet jack connects to the Zynq PS GEM through MIO. Linux on the ARM runs the network stack.
THE COMPARISON
Baseline: Python recvfrom/sendto per datagram. Candidate: C recvmmsg/sendmmsg, batching up to 32.
THE CLAIM
Does batched Linux socket I/O improve measured UDP echo performance on this board, and what happens to loss, latency, and CPU?
Important boundary
Both versions run on the PS. The PL is not carrying Ethernet traffic in this selected project.
This keeps the comparison testable on the onboard jack and avoids claiming unavailable PL connectivity.

## Slide 3
01 | SYSTEM CONTEXT
Where the packets actually go
The built-in connector is real hardware; only the server implementation changes.
PYNQ-Z2 | PS UDP performance study
03
01
Host PC
Python benchmark
creates UDP datagrams
02
Ethernet link
RJ45 cable +
switch (if used)
03
PHY + PS GEM
RTL8211E PHY →
PS Ethernet MAC
04
Linux network
Driver + IP/UDP
kernel stack
05
Server process
Python baseline OR
C batched candidate
Controlled path
Same board • same PS GEM • same Linux kernel • same host test program
The Ethernet hardware and kernel stack are controls—not the experiment.

## Slide 4
02 | BACKGROUND
Technical literature survey
The sources support the design choices; they do not predetermine the result on this board.
PYNQ-Z2 | PS UDP performance study
04
Source
Established point
Design implication
Python socket docs [1]
Python exposes the standard socket API for UDP; it is a usable high-level baseline.
Keep socket semantics and packet bytes the same.
Linux recvmmsg [2]
One syscall can receive multiple messages; Linux documents potential application performance benefits.
Candidate receive path batches queued datagrams.
Linux sendmmsg [3]
One syscall can submit multiple messages; partial sends must be handled.
Candidate transmit path retries unsent tail of a batch.
Linux NAPI docs [4]
NIC/kernel polling and interrupt moderation also affect batching and latency.
Keep kernel/link fixed; application batching is only one layer.
PYNQ docs [5]
PYNQ supports Python productivity and lower-level C when efficiency matters.
Motivates an embedded Python-versus-C comparison.
RFC 2544 [6]
Comparable performance reports require defined tests and conditions.
Fix packet sizes, duration, run order, repetitions, and report metrics.
Survey scope: official API / platform documentation + benchmarking guidance (not a claim of exhaustive academic review).

## Slide 5
02 | BACKGROUND
The project gap and research question
State the gap narrowly and defensibly: this is a target-board evaluation gap, not a claim that no one has studied batching.
PYNQ-Z2 | PS UDP performance study
05
What documentation already gives us
APIs for ordinary and batched UDP I/O
A plausible mechanism: fewer per-message syscalls
Warnings that kernel/NIC behavior also shapes results
What this project must measure
Effect on PYNQ-Z2 PS GEM + its installed Linux image
Throughput, loss, latency, and server CPU together
Whether a batched candidate helps under the same offered load
Research question
On the PYNQ-Z2, does C batched UDP I/O outperform the Python per-datagram baseline at equal packet sizes and offered load?
Gap defined by this project: no controlled PYNQ-Z2 measurements are recorded yet. The answer is open until board tests are run.
H0: batching does not improve median reply rate. H1: it improves rate/goodput without increasing loss or corruption.

## Slide 6
03 | DESIGN
Proposed system and components
The two implementations share one PS/Linux stack and one benchmark protocol.
PYNQ-Z2 | PS UDP performance study
06
PYNQ-Z2 board
Zynq-7000 ARM Cortex-A9 runs Linux; onboard PHY + PS GEM carry packets.
Python baseline
Blocking UDP socket; receive one datagram and echo it per loop iteration.
C candidate
Linux recvmmsg/sendmmsg; reusable message arrays; up to 32 datagrams per batch.
Host benchmark
Sends sequenced payloads in fixed bursts; checks replies and timestamps RTT.
Metrics + report
JSONL raw runs, median comparison, integrity/loss checks, server CPU evidence.
Network setup
Wired host-to-board path; same switch/cable, port, negotiated speed, and IP config.
No custom MAC/PHY RTL is required for the selected PS-based experiment.

## Slide 7
03 | DESIGN
Baseline and candidate: one controlled A/B test
The only intentional independent variable is the server implementation.
PYNQ-Z2 | PS UDP performance study
07
CONTROLLED INPUTS
Same host benchmark and code
Same UDP packet format
Same payload length and 32-packet burst
Same test duration and socket-buffer request
Same board, Linux, link, and network path
A • Python baseline
recvfrom → validate → sendto
B • C batched candidate
recvmmsg → validate → sendmmsg
COMPARE OUTPUTS
Valid unique replies per second
UDP payload goodput (Mbps)
Loss / corrupt / duplicate replies
Mean, p50 and p95 RTT
Board process CPU time / CPU use
One server at a time; alternate run order to reduce warm-up / drift bias.

## Slide 8
03 | DESIGN
What changes in the code?
The experiment targets application-to-kernel call frequency, not the Ethernet PHY or IP stack.
PYNQ-Z2 | PS UDP performance study
08
BASELINE | PYTHON
while running:
payload, peer = sock.recvfrom(1473)
if len(payload) <= 1472:
sock.sendto(payload, peer)
One receive + one send call per datagram
CANDIDATE | LINUX C
n = recvmmsg(fd, rx, 32, MSG_WAITFORONE, NULL)
validate each received datagram
sent = 0
while sent < valid_count:
sent += sendmmsg(fd, &tx[sent],
valid_count - sent, 0)
Up to 32 queued messages per syscall; handle partial sends
Hypothesis: fewer per-datagram user/kernel transitions can reduce CPU cost and raise packet rate when the server is the bottleneck.

## Slide 9
04 | EXPERIMENT
Methodology: make the comparison fair
Pre-register the main metric and keep all other variables fixed.
PYNQ-Z2 | PS UDP performance study
09
1
Inspect
Record PYNQ image, kernel, CPU architecture, GCC, link speed/duplex, socket buffers.
2
Validate
Run integrity tests against both servers; confirm exact echoes before load testing.
3
Warm up
Warm each server and path equally; do not mix warm-up packets into timed samples.
4
Measure
5+ paired runs per payload; alternate A/B order; save each JSON record.
5
Analyze
Compare medians and variation; examine packet loss, RTT, CPU, and errors.
6
Report
Keep raw logs, environment, commands, captures, plots, and limitations.
Repeat for 64 B, 512 B and 1472 B payloads; same 32-packet host burst and 10 s offered-load window.

## Slide 10
04 | EXPERIMENT
What exactly will be measured?
Application-level metrics are not a substitute for PHY line-rate testing.
PYNQ-Z2 | PS UDP performance study
10
GOODPUT
Unique echoed payload bits / timed seconds
Mbps = unique_replies × payload_bytes × 8 / seconds / 10⁶
PACKET RATE
Count only valid, unique echoes
replies/s = unique_replies / timed seconds
LOSS
Sent sequences with no valid echo after drain
loss % = (sent − unique_replies) / sent × 100
LATENCY
Host monotonic send-to-valid-echo time
Report mean, p50, p95; compare under same offered load
CPU COST
Server process CPU time + Linux CPU monitor
Report CPU seconds and average utilization separately
INTEGRITY
Sequence, exact length and payload bytes
Any corruption / unexpected duplicate is a correctness failure
Use the same timer boundary and drain interval for A and B; disclose that loopback throughput includes host and Linux overhead.

## Slide 11
04 | EXPERIMENT
Test matrix and controlled variables
A small matrix is easier to repeat, audit, and explain in a viva.
PYNQ-Z2 | PS UDP performance study
11
Variable
Plan
Reason
Server
Python baseline vs batched C
Independent variable
Payload size
64 B / 512 B / 1472 B
Small, mid-size, near-MTU behavior
Host burst
32 datagrams (both versions)
Creates queue opportunities for batch receive
Timed load
10 s + identical 1 s reply drain
Common throughput window and loss accounting
Socket buffers
Request 4 MiB; record actual values
Avoid hidden A/B buffer mismatch
Repetitions
At least 5 paired runs per size
Expose run-to-run variability
Order
Alternate Python→C and C→Python
Reduce warm-up / thermal / time-order bias
Environment
Same wired host, board image, link, port, background load
Hold non-treatment variables constant
Record negotiated Ethernet rate; do not call application goodput “1 Gb/s line rate.”

## Slide 12
05 | EVALUATION
Expected change vs verified improvement
Separate the mechanism you implemented from what the data proves.
PYNQ-Z2 | PS UDP performance study
12
Implementation delta
Potential benefit (hypothesis)
Evidence required
recvmmsg() receives multiple queued UDP datagrams in one call
Fewer receive syscalls per packet; lower server CPU per datagram
C process CPU + packets/s under matched traffic
sendmmsg() sends multiple datagrams in one call
Fewer transmit syscalls; higher reply rate at high packet rate
Median goodput/replies/s; verify partial-send handling
Reusable arrays and buffers
Less per-packet setup/allocation work in the loop
Code review + CPU / rate data; no payload corruption
One measurement harness for A and B
Results become directly comparable and reproducible
Same JSON fields, sequence checks, config and test schedule
Candidate ≠ proven faster. Only board measurements can support an improvement claim.

## Slide 13
05 | EVALUATION
How to prove the candidate is better
Define success before looking at the results.
PYNQ-Z2 | PS UDP performance study
13
1
Correctness gate
100% exact payload echoes in the integrity test; zero corrupt replies in benchmark.
2
Performance gate
Median goodput or valid replies/s improves consistently across paired trials.
3
Reliability gate
No unacceptable loss increase; disclose loss and all excluded/failed runs.
4
Trade-off gate
Show RTT and CPU alongside throughput—do not hide regressions.
Report the paired change
Improvement % =
(median_C − median_Python)
÷ median_Python × 100
For loss, report percentage-point change. Show all repeated values or a box plot—not only the best run.
If results are noisy or overlap, conclude “no clear improvement in this setup” and discuss why.

## Slide 14
06 | EXECUTION
Tools and what each one proves
This PS-based project does not need Vivado for its Ethernet data path.
PYNQ-Z2 | PS UDP performance study
14
Tool
Use
Evidence produced
PYNQ-Z2 + Linux
Run both servers on ARM/PS GEM
Board-side behavior and CPU environment
GCC on PYNQ
Build C candidate using documented flags
Compiler and target environment are recorded
Host Python 3
Loopback + same load generator for both servers
Integrity, sequence counts, RTT and rate
compare_results.py
Compute median metrics from JSONL files
Reproducible A/B summary
top / pidstat
Observe server CPU under load
CPU-use trade-off (if available)
Wireshark
Capture host Ethernet interface
Check ARP, UDP source/destination and packet sizes
Git + results/
Version code, raw logs, configs and report
Reproducibility and review trail
Vivado/JTAG is not in scope: it cannot route the onboard PS Ethernet jack into custom PL logic.

## Slide 15
06 | EXECUTION
Execution plan and deliverables
A sequence that gets a defensible result before presentation day.
PYNQ-Z2 | PS UDP performance study
15
A
Environment check
Boot/network, identify IP and link, verify GCC + Linux APIs.
Log system versions
B
Build + functional test
Compile C server; run exact-echo test against A and B.
Save commands/logs
C
Benchmark
3 payload sizes × 5+ repeats × alternating A/B order.
Save JSONL files
D
Analyze
Compare medians, run-to-run spread, loss, RTT and CPU.
Create figures/table
E
Conclude
Explain whether batching helped on this setup and limitations.
Complete results report

## Slide 16
07 | RESULTS
Results slide: fill only after board testing
No board measurements are available yet. This slide is a reporting template, not a result.
PYNQ-Z2 | PS UDP performance study
16
DATA PENDING
Payload
Variant
Median replies/s
Goodput Mbps
Loss %
p95 RTT ms
CPU %
64 B
Python baseline
—
—
—
—
—
64 B
Batched C
—
—
—
—
—
512 B
Python baseline
—
—
—
—
—
512 B
Batched C
—
—
—
—
—
1472 B
Python baseline
—
—
—
—
—
1472 B
Batched C
—
—
—
—
—
Do not report localhost smoke-test values as PYNQ-Z2 performance.

## Slide 17
07 | RESULTS
Limitations to acknowledge in the viva
Clear limitations strengthen the credibility of the conclusion.
PYNQ-Z2 | PS UDP performance study
17
Not raw Ethernet capacity
Application goodput includes host, kernel, driver and socket costs.
Linux version matters
recvmmsg/sendmmsg availability and implementation depend on the board image/kernel.
Host can bottleneck
A saturated generator or receiver can hide server differences.
Burst size changes load
Fixed host burst may favor batching; disclose and test additional burst settings if time permits.
One board is one sample
Conclusions apply to this hardware/software configuration, not every Linux system.
CPU metrics differ
Process CPU time and system-wide utilization are different; label the measurement method.
A useful result can be “no measurable benefit under this offered load”—that still answers the research question.

## Slide 18
08 | CLOSE
Take-away and references
What makes the project stronger is the experimental design and honest evidence—not a promised speedup.
PYNQ-Z2 | PS UDP performance study
18
THE PLAN
Keep the board and network path fixed.
Change Python per-packet I/O to Linux C batched I/O.
Prove correctness first; then compare rate, loss, latency and CPU over repeated runs.
No improvement is claimed until board data supports it.
REFERENCES
[1] Python socket API — docs.python.org/3/library/socket.html
[2] Linux recvmmsg(2) — man7.org/linux/man-pages/man2/recvmmsg.2.html
[3] Linux sendmmsg(2) — man7.org/linux/man-pages/man2/sendmmsg.2.html
[4] Linux NAPI — docs.kernel.org/networking/napi.html
[5] PYNQ introduction — pynq.readthedocs.io/en/latest/
[6] RFC 2544 — rfc-editor.org/rfc/rfc2544 (methodology inspiration; this is not RFC2544 compliance)
[7] AMD UG585 — docs.amd.com/v/u/en-US/ug585-Zynq-7000-TRM
Sources accessed 7 Oct 2026. Platform-specific facts and all performance values should be verified against the actual board image and measurements.